# Hidden Function Settings

The table below shows the Hidden Function Settings for the FT100.  The Yaesu Global column has suggested values from Yaesu  to set them back to an average value should they become lost or corrupted.  Radio #1 and Radio #2 are settings from radios contributed by two U.S. customers for comparison.  The blank 'Your Radio' column is intended for you to print out this form and fill in with your own settings in the event that you start making changes and want to get back to your radio's original settings.

To view your hidden function settings, power up the radio while pressing A, B, and C simultaneously.  Let go of all buttons and then press the FUNC key for 1/2 second.  This will open up all function settings for editing, i.e., the normal ones and the hidden ones as well.  If you don't see the hidden functions, you will need to scroll down past regular menu item 01 or beyond regular menu item 66 to get to them.

A word of caution is in order.  If you intend to make any changes, record all the original values first.  Most of these settings are unique to each  radio and are determined by using  alignment procedures described in the FT100 Service Manual.  Also, DO NOT SCROLL THROUGH  THE LIST OF ALTERNATE COUNTRY SETTINGS in F57 and F58  unless you don't mind having your radio do a complete reset where it will lose all of the VFO,  memories, and regular menu settings.  It's not necessary to save the setting.  Just scrolling through the various country choices for settings will cause this to happen so resist the temptation to do it unless you don't mind re-entering all of your regular menu and memory settings back into the radio.  You may check to see what your settings are for F57 and F58, but you'll wipe out other information if you try to look at other settings that are available for those functions.   If you're curious, alternate settings are shown in the table below.

The reset should not affect the hidden function values but make sure to copy them down in a safe place just in case.  It is basically the same as both reset procedures as stated on page 102 of the manual.

| Function | Yaesu Global | Radio #1 | Radio #2 | My Radio | Description |
| --- | --- | --- | --- | --- | --- |
| F01 | 166 | 166 | 166 |  | 144 RF GAIN |
| F02 | 166 | 166 | 166 |  | 430 RF GAIN |
| F03 | 100 | 098 | 103 |  | HF RX IF G |
| F04 | 108 | 112 | 107 |  | 50 RX IF G |
| F05 | 119 | 108 | 110 |  | 144 RX IF G |
| F06 | 108 | 082 | 099 |  | 430 RX IF G |
| F07 | 187 | 144 | 192 |  | S FULL SCALE |
| F08 | 009 | 033 | 003 |  | SSB SQL |
| F09 | 074 | 088 | 082 |  | FM N SQL |
| F10 | 077 | 056 | 072 |  | FM RF SQL |
| F11 | 026 | 023 | 028 |  | HF IC ALC |
| F12 | 023 | 022 | 024 |  | V/UHF IC ALC |
| F13 | 020 | 026 | 019 |  | HF PO 10W |
| F14 | 080 | 083 | 078 |  | HF PO 50W |
| F15 | 122 | 123 | 125 |  | HF PO 100W |
| F16 | 019 | 025 | 017 |  | 50 PO 10W |
| F17 | 040 | 045 | 038 |  | 50 PO 20W |
| F18 | 080 | 083 | 074 |  | 50 PO 50W |
| F19 | 122 | 123 | 121 |  | 50 PO 100W |
| F20 | 063 | 063 | 063 |  | 70 PO 10W <<< 70 MHz |
| F21 | 056 | 065 | 063 |  | 144 PO 20W |
| F22 | 110 | 120 | 119 |  | 144 PO 50W |
| F23 | 152 | 139 | 150 |  | 430 PO 20W |
| F24 | 075 | 076 | 068 |  | 1.8 TX IF G |
| F25 | 070 | 069 | 063 |  | 3.5 TX IF G |
| F26 | 063 | 063 | 057 |  | 7 TX IF G |
| F27 | 063 | 063 | 057 |  | 10 TX IF G |
| F28 | 067 | 067 | 060 |  | 14 TX IF G |
| F29 | 073 | 071 | 066 |  | 18 TX IF G |
| F30 | 069 | 072 | 065 |  | 21 TX IF G |
| F31 | 071 | 072 | 067 |  | 24 TX IF G |
| F32 | 086 | 075 | 069 |  | 28 TX IF G |
| F33 | 097 | 104 | 085 |  | 50 TX IF G |
| F34 | 127 | 127 | 127 |  | 70 TX IF G <<< 70 MHz |
| F35 | 084 | 097 | 092 |  | 144 TX IF G |
| F36 | 120 | 093 | 084 |  | 430 TX IF G |
| F37 | 202 | 196 | 199 |  | ALC METER |
| F38 | 164 | 170 | 158 |  | HF PO METER |
| F39 | 166 | 172 | 160 |  | 50 PO METER |
| F40 | 109 | 105 | 102 |  | 144 PO METER |
| F41 | 057 | 063 | 058 |  | 430 PO METER |
| F42 | 035 | 034 | 033 |  | HF REV ALC |
| F43 | 041 | 034 | 048 |  | 50 REV ALC |
| F44 | 127 | 127 | 127 |  | 70 REV ALC <<< 70 MHz |
| F45 | 179 | 173 | 162 |  | 144 REV ALC |
| F46 | 035 | 060 | 034 |  | 430 REV ALC |
| F47 | 154 | 141 | 169 |  | SWR METER |
| F48 | 230 | 230 | 230 |  | OVER HEAT 1 |
| F49 | 235 | 235 | 235 |  | OVER HEAT 2 |
| F50 | 141 | 166 | 141 |  | CW CAR LEVEL |
| F51 | 105 | 113 | 108 |  | AM CAR LEVEL |
| F52 | -27.090 | -32.470 | -30.130 |  | FM TX FREQ |
| F53 | -0.200 | 0.110 | 0.110 |  | TRX LSB CAR |
| F54 | -0.190 | -0.010 | -0.130 |  | TRX USB CAR |
| F55 | blank | blank | blank | blank |  |
| F56 | blank | blank | blank | blank |  |
| F57 | USA DO NOT | USA CHANGE | USA !!!! | USA See Above | DESTINA HF < JPN,JAIA,STD, EU,FRAN,BEL,GER,USA,AUS,UT |
| F58 | USA DO NOT | USA CHANGE | USA !!!! | USA See Above | DESTINA V/U < same as HF> |
| F59 | blank | blank | blank | blank |  |